## Slide 1: Confidential Computing for OpenPOWER
Guerney D. H. Hunt*, Ramachandra Pai†, Michael V. Le*, Hani Jamjoom*, Sukadev Bhattiprolu†,
Rick Boivie*, Laurent Dufour†, Brad Frey†, Mohit Kapur*, Kenneth A. Goldman*, Ryan Grimm†,
Janani Janakirman†, John M. Ludden†, Paul Mackerras†, Cathy May†, Elaine R. Palmer*, Bharata
Bhasker Rao†, Lawrence Roy*‡, William A. Starke†, Jeff Stuecheli†,Enriquillo Valdez*, Wendel
Voigt†
*IBM Research †IBM ‡Oregon State University, USA
Eurosys 2021
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 2: Acknowledgements
IBM is a registered trademark of International Business Machines Corporation in the United States and/or other countries. Linux is a registered trademark of Linus Torvalds. Other company, product, and service names may be trademarks or service marks of others.
IBM Research/ October 1, 2019 / © 2018 IBM Corporation
The authors would like to acknowledge the significant contributions to this project by Mike Anderson, Thiago J. Bauermann, Christopher J Engel, Ronald Kalla, Memmet Kayaalp, Jens Leenstra, Dimitrios Pendarakis, Peter A. Sandon, and Sarah Wright. Without their efforts this project would not have been successful.
This work represents the view of the authors and does not necessarily represent the view of IBM. All the code discussed in this presentation has been Open Sourced.

## Slide 3: Secure computing technology from IBM
Includes
IBM 4758 circa 1998
IBM “Secure Blue” Secure Processor Technology (circa 1999- 2005)
IBM proposed the SecureBlue++ trusted execution environment circa 2011
HWMAC: Hardware-Enforced Fined-Grained Policy-Driven Security, IBM Research Report RC25155, 2011
DHS funded project, contract number FA8750-12-C-0243, Hardware-Support for end-to-end Trust circa2013 – 2016
Secure Service Containers for IBM Z and LinuxOne (circa 2016)
IBM Secure Execution for LinuxOne (Circa 2019)
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 4: Confidential Computing
  TEEs are supported on multiple platforms and generally based on hardware and firmware/software support
  Example of TEEs include IBM Z Secure Execution for LinuxOne, AMD SEV, Intel SGX, Intel TDX, and others
  Properly using a TEE in the cloud enables the user to exclude the cloud provider from their Trusted Computing Base (TCB)
IBM Research/ October 1, 2019 / © 2018 IBM Corporation
Confidential computing exploits a Trusted Execution Environment (TEE) to enable a user to confidentially utilize a computing infrastructure

## Slide 5: Current commercial TEEs
 | Intel SGX | AMD SEV | IBM Z SE | IBM PEF | Intel TDX
Open Source |  |  |  |  | 
Sharing Secure Memory |  |  |  |  | 
App. Transparency |  |  |  |  | 
Attestation Model | R | R | L | L | R
Not yet available
Intel SGX, is a process-based TEE that requires software support to achieve application transparency
AMD SEV is a VM-based TEE which natively supports application transparency
Both Intel SGX and AMD SEV use remote attestation
Neither Intel SGX nor AMD SEV allow sharing of secure memory between TEEs
PEF is the only open-source TEE for server class machines
IBM PEF, like AMD SEV, and Z Secure Execution for LinuxOne is a VM-based TEE
  Local attestation may scale better than remote attestation in cloud scenarios
When available Intel TDX will be a VM-based TEE

## Slide 6: Objectives
  Create an open-source server class TEE for OpenPOWER
  Balance between isolation and confidentiality
  Minimize the number of new elements introduced
  Create Secure Virtual Machines (SVMs) which have more protection than Normal Virtual Machines (NVMs)
  Simplify TEE life-cycle management for the cloud
  Balance the needs of the cloud provider, cloud user, and platform manufacturers
  Zero or minimal impact on NVMs on a system that is TEE capable
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 7: Threat model
Attack Vectors
  VMs
  SVMs
  Hypervisor (rogue or compromised)
  Operator
  Physical attack
Apps
VM
Guest
VM
Apps
SVM
Guest
VM
Apps
VM
Guest
VM
Linux / KVM
Protected Execution Ultravisor (Firmware)
HARDWARE
IBM Research/ October 1, 2019 / © 2018 IBM Corporation
Untrusted
Trusted

## Slide 8: Approach
Hardware enforced access control for isolation
  Memory is partitioned into secure and non-secure
Cryptography for integrity and confidentiality
Create new POWER processor state: “Ultravisor state”
  Higher privileged than hypervisor state
  Everything that affects security is controlled by new firmware, Ultravisor
  Enables SVMs
Function and purpose of Hypervisor unchanged
  Utilizes Ultravisor to accomplish some tasks
Problem
Supervisor (OS)
Hypervisor
Ultravisor
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 9: Ensuring isolation, confidentiality and integrity
New state
With new open-source firmware, Ultravisor
      The Ultravisor maintains the isolation and security of the SVMs and their associated data
      Ultravisor receives all hypercalls and asynchronous interrupt for SVMs
      Not complex, no user interface
Hypervisor can only see SVM memory in encrypted state.
      Unless explicitly shared with hypervisor by SVM
    Added ultracalls which go directly to the Ultravisor
Interface | Number
Ultracalls | 20
New hypercalls | 6
Existing hypercalls | 152

## Slide 10: Affect on VMs/SVMs
Secure VMs (SVMs) and Normal VMs run on the same hardware
SVMs and VMs both get services from the hypervisor
      All hypervisor calls from an SVM go to the Ultravisor
      An SVM can share unprotected memory with the hypervisor
      Bi-directional protection for SVMs from other SVMs, the Hypervisor, and NVMs
      User verification of integrity of TEE
SVM images are created with new tooling
      The creator of an SVM image supplies a public key associated with a target machine where the SVM is authorized to run
A Secure VMs image is deployed as a normal VM and uses an Enter Secure Mode (ESM) ultracall to transition into secure mode
Virt I/O devices supported with bounce buffering
      SVM must protect data prior to utilizing hypervisor
Hypervisor
Protected Execution Ultravisor
Untrusted
Trusted
Secure VM preparation tool
Public Key
Secure VMs
Normal VMs
Storage
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 11: Impact on the hypervisor
The Ultravisor is higher privileged than the hypervisor
The hypervisor (Linux/KVM) has been paravirtualized to operate properly with the Ultravisor
      Most of the required changes are in the architecture dependent sections of the hypervisor
When the hypervisor needs to update the partitioned scoped page table, it asks the Ultravisor for assistance
When the hypervisor is returning to an SVM it asks the Ultravisor to complete the return
The Heterogeneous Memory Management (HMM) was enhanced to enable the Ultravisor to associate secure pages with a secure VM
Hypervisor
Protected Execution Ultravisor
Untrusted
Trusted
Secure and trusted boot
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 12: Approach at the hardware/firmware level
Target machine’s private key is in the TPM
      Ultravisor uses the TPM to access the symmetric seed that protects the SVM
      Ultravisor has a secure channel through hypervisor to the TPM
The hardware enforces access to secure memory
      Only software running in secure mode can access secure memory
      After boot, only the SVMs and Ultravisor run in secure mode
The Enter Secure Mode (ESM) ultracall causes the Ultravisor to verify the NVM
      ESM Operand used to verify NVM
Non-Volatile memory
Trusted Platform Module
Private Key
Hypervisor
Protected Execution Ultravisor
Untrusted
Trusted
Secure and trusted boot
Normal Memory
Secure Memory
CPU
Protected Execution Facility
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 13: ESM Operand
Ultravisor only has access if SVM is authorized to run on this target system
The Ultravisor uses the TPM to access the symmetric seed
  From which it generates a symmetric key and HMAC key
Each lock box is an index and a wrapped key (index = hash of public key)
  Wrapped key: the symmetric seed encrypted with the target machine’s public key
Integrity information for verification
Pass phrase
Customer data
IBM Research/ October 1, 2019 / © 2018 IBM Corporation
HMAC of Payload block
CDn: Customer Data
CD1: Passphrase for encrypted filesystem
Integrity Information: Kernel, Kernel command line, Initramfs, RTAS
Symmetric seed encrypted for Machine B
Symmetric seed encrypted for Machine A (primary)
Lock box
Payload
Payload block

## Slide 14: Verifying integrity of system and SVM
Verification relies on secure and trusted boot to generate a value representing the hardware vendor and the hardware state
During verification, the Ultravisor uses the TPM to confirm the values specified by creator of the SVM
Verification relies on the creator of the SVM to specify which machine(s) is authorized to run SVM
    This is done by specifying the public key of a target machine and a PCR 6 value/policy
    A lockbox give a target machine access to the symmetric seed protecting the SVM
    If the Ultravisor does not find a valid Lockbox, the machine is not authorized
    If the PCR6 value and policy are not correct the Ultravisor will not have access to the symmetric seed
Each time the SVM starts, the state of the system and the integrity of the SVM are verified

## Slide 15: Balancing needs among cloud providers, users, and equipment manufactures
Some Cloud applications require (or are more easily facilitated by) sharing of secure memory between TEEs
OpenPOWER manufactures supply firmware updates to their customers to fix issues.
Cloud providers want to be able to add and subtract machines from their infrastructure without affecting TEEs
    This includes transparently applying firmware updates
Users of TEE often want to be able to exclude their cloud provider from their TCB
    Some customers want to retain control of their secrets
Users of TEE want to be able to specify the requirements of an acceptable platform
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 16: Cloud integration
Design allows the authorization for a TEE to execute on a particular machine to be inserted just prior to execution
Proposes to utilize a Hardware Security Module (HSM) to generate the authorization, which meets creator’s specification
HSM is controlled by creator of SVM but part of the cloud provider’s infrastructure
Allows creator of SVM to specify requirements that target system must fulfill

## Slide 17: Evaluation
Our initial work focused on the functionality and security of PEF, not performance optimizations
  Functionality was tested by running multiple virtual machines with different workloads
We investigated the difference between NVM and SVM performance
We ran our evaluation on IBM AC 925s configured to run with PEF enabled

## Slide 18: Spec CPU Intrate and Intspeed

## Slide 19: Real World Application Apache (ab)

## Slide 20: Evaluation Summary
The speccpu and specint measurements are very similar
There was no significant impact of boot time
Network and block performance test showed impact from PEF
  As expected, smaller blocks have more overhead than larger blocks
  The extra overhead appears to be because of bounce buffering

## Slide 21: Complexity of Approach
Component | KLOC | K bytes
Ultravisor | 39 | 897
TSS | 37 | 263
Kernel/KVM | 3000 | 2500
Component | Lines of Code
Host Kernel Paravirtualization | 248
Host Kernel HMM | 267
Secure VM Kernel enablement | 461
QEMU | 292
Linux Support
Code Size

## Slide 22: Limitations
Protected Execution Facility does not currently support
Transactional memory
Applications that use transactional memory will crash in an SVM
Ultravisor has not implemented
  Suspend
  Resume
  Migration
  Over commit of secure memory
  Dedicated devices to SVMs
  XIVE interrupt controller
  Sharing of secure memory
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 23: Contact Information
Guerney D. H. Hunt: gdhh@us.ibm.com
Hardware: contact your OpenPOWER vendor or IBM representative
OpenPOWER foundation: https://openpowerfoundation.org/
Instruction for Building : https://github.com/open-power/ultravisor/wiki/How-to-build-and-run-Secure-VM-using-Ultravisor-on-a-OpenPOWER-machine
Git repositories for artifacts
Ultravisor: https://github.com/open-power/ultravisor
SVM tools: https://github.com/open-power/svm-tools
PNOR1: https://github.com/rampai/op-build
Artifacts independently Verified
1 PNOR originally was Processor NOR flash, it now just refers to the firmware load for the processor

## Slide 24
Thanks very much for attending this talk.
Questions?
IBM Research/ October 1, 2019 / © 2018 IBM Corporation

## Slide 25
IBM Research/ October 1, 2019 / © 2018 IBM Corporation